## Slide 1: IETF 99 Hackathon
SDN Applications for microwave radio link via IETF YANG Data Model

## Slide 2: YANG model for Microwave radio link
A design team was set up in IETF CCAMP WG to work on microwave radio links Yang Modeling
The framework draft (draft-ietf-ccamp-microwave-framework) was adopted by CCAMP WG:
https://datatracker.ietf.org/doc/draft-ietf-ccamp-microwave-framework/
“Microwave Modelling at CCAMP WG”in IETF journal:
https://www.ietfjournal.org/working-group-update-microwave-modelling-at-ccamp/
June, 2016
December, 2016
March, 2017
The YANG model draft (draft-ietf-ccamp-mw-yang) was adopted by CCAMP WG: https://datatracker.ietf.org/doc/draft-ietf-ccamp-mw-yang/
July, 2017
Hackathon in IETF 99 to validate the microwave model
April, 2017

## Slide 3: What was developed in hackathon
Purpose: To validate the model defined in draft-ietf-ccamp-mw-yang-01
Developed in hackathon:
  MW YANG model in ODL controller
  Two applications: Energy Efficiency and Dynamic frequency control
App 1:
Energy efficiency
App 2:
Dynamic frequency control
SDN controller – ODL based
MW YANG
model
draft-ietf-ccamp-mw-yang
Day Time
Night Time
Power consumption
Traffic
Peak time
Off-peak time
With energy efficiency
f1
f2
to save power consumption when traffic is low
to control the interference
App 1: Energy efficiency
App 2: Dynamic frequency control
SNIR
Frequency
f1
f2
Alert threshold
！
Low SNIR

## Slide 4: Achievement & Next step
Achievement:
  Added implementation of IETF mw YANG model in open source software (ODL)
  Validated the mw YANG data model, and developed & tested the two use case applications successfully
  Bring industry vendor competitors and university to work together
  Attracted three first IETFers
Lesson learned:
  Need to optimize the way of rx-frequency configuration
  Require additional statistics e.g. link utilization information
  Use of REST APIs instead of RESTCONF
Next step:
  Cooperate with other packet interfaces e.g. Ethernet
  Add more statistics either in mw YANG model, or in an ETH YANG model
  If possible, contribute the model implementation to open source project

## Slide 5: Thanks for the team!
Team members:
On site: Min Ye, Jinchao Pang, Jonas Ahlberg, Tamas Radocz, Xi Li, Haomian Zheng, Zheyu Fan, Carlos J. Bernardos
Remote: Koji Kawada, Daniela Spreafico, Marko Vaupotic